By Jaseung Ku
Updated 4/19/2019

Terminology
Image = Individual pattern on a mask
Die = chip

Chip design rules: Follow these rules to make life easier :)
1. Make everything as a cell for easy modification and modularity. A cell is like a class in program language, so all the instances will be changed if the cell is changed.
2. Place the center of each image bounding box at coordinates of integer multiples of 8. (Note: If an image goes to multiple positions, the coordinates should be multiples of 8 to use the same flux trap pattern, e.g. capacitors at multiple locations.
3. Patch bounding boxes are used in creating base flux traps on the die. Also, they shouldn’t overlap not to have multiple flux traps.
4. (optional if #2 is enforced) Each image has its own flux trap. For this, the center of the image in chip coordinate should be used to calculate how much flux trap should be offsetted. Note, if the center coordinates are multiples of 8, then no offset is needed.
5. Patch bounding boxes can be made later from image bounding boxes after flattening all cells, since everything is a cell.
6. All the images should be within 21000 x 21000 um2.
TO-DO: there are specific boundaries outside of which ASML can’t read. Create this pattern in GDS.
7. Each image should be at least 750 um apart.
8. Before creating flux trap, create backup (klayout could crash).
9. Avoid having two instances(or bounding boxes) touch. Leave a gap so as to be able to make patterns slightly overlapping with images.
10. When creating images, make all patterns lie within a Image BBox. The size of Image BBox is used in ASML to blade off.

Layer info
It is very important to understand first what each layer is used for and to use the right layer for whatever you draw in Klayout.

Convention
A layer is specified by N/M, where N=layer number, M = datatype number.

In 0 layer, anything that doesn’t appear on the mask, e.g. outlines
In 1 layer, anything that appears on the mask, e.g. flux trap.
Data type defines what kind of stuff goes on an each layer.

Layer definition

Layer name	Layer/Data type	Description
Patch BBox	0/0	Patch bounding box that defines area in which an image is patched in the base pattern of a die. Also, it’s used when creating flux traps.
­Keepout	0/1	Keepout area that keeps out flux traps. CPW and bias line cells should have keepout.
CPW path	0/2	Path that turns into CPW by a macro or python script
Image BBox	0/3	Image bounding box for each image. This sets boundary of image within which flux traps are created. The size of Image Bbox should be the same as that of Patch BBox since an image (as a cell) is patched into Patch BBox during ASML stepper job.
Die BBox	0/4	Die bounding box. This may set the size of actual die, e.g. 6.25x6.25 or 8x8 mm chip / Depreciated. Use Image Bbox.
Image	1/0	Any pattern to be written on the mask
Flux trap	1/1	Flux trap holes

Useful setting
1. File menu → Setup
a. Default Grids : 1, 0.1, 0.01, 0.001
b. Snapping : Choose both “Snap to grid” and “Snap to edge/vertex”.
2. View menu → Select Top Level Objects

Tentative procedure for designing a mask
1. Outline a circuit. Determine a base pattern in a die which can’t be changed and images which will be patched into the base pattern during ASML job.
2. Make images and make them all cells. A die cell has (fixed) base pattern and patch bounding boxes.
IMPORTANT:
a. Each cell should have the origin in the center of Image Bounding Boxes.
b. Each image shouldn’t have child cell (flatten cell and remake cell if	necessary).
3. Lay out images for a mask. Make sure there is at least 750um spacing between images.
4. Copy all instances and past into a new cell for a mask?
5. Create flux trap.
5. Flatten the new cell and save it as GDS2 file.

Note on Flux trap creation
1. For GND flux trap on a die
Create an instance of fluxTrap_8x8mm and then fluxTrap array. Flatten it and center it. Do boolean operation in layer menu. CHOOSE “no undo buffering”. Otherwise, gds file could be corrupted to 0 byte.
2. For flux trap in the images
Each image must be a cell. Even a cell with a sub-Pcell is ok. Found that the resulting cell has flattened structure. No need to flatten subcells before creating flux traps.

Design Rule Check (DRC)
TO-DO: set up DRC. May need a script.
1. For each cell, origin in the center of bounding box.
2. a No overlap between objects on the same layer, but they can touch.
    b. No overlap between objects in “Image” layer and flux traps.
3. Patch bound boxes should be touching. We need about 500nm of image extension into the patch bounding box to avoid unwanted break that could be created during mask creation.
4. The center of image bounding box is multiple of 8.