Design a mask using Klayout
By Jaseung Ku
Updated 8/4/2019

Terminology
Image = Individual unit of pattern on a mask. We need to record 1) x and y coordinate of the center and 2) the size of bounding box of each image to create an ASML job file.
Die = A unit chip after dicing
Die Image = Image which is used for a base image of a die.
Image distribution keepout box = placeholder box in KEEPOUT layer for image distribution purpose

Chip design rules: Follow these rules to make life easier :)
Making images:
1. Make everything as a cell for easy modification and modularity. A cell is like a class in program languages, so all the instances, once created, will be changed accordingly if the cell is modified.
2. When creating images, make all patterns lie within an image bounding box. The size of the bounding box is used in ASML to blade off.
3. Each image must have at minimum the following two layers: IMAGE and IMAGE BBOX.

Making a full mask image:
TO-DO: there are specific boundaries outside of which ASML can’t read. Create this pattern in GDS.
1. All the images should be within 21000 x 21000 um2.
2. Each image should be at least 750 um apart.

Make a Die Image:
1. Image distribution keepout boxes are used to keep out flux traps in a die. They must neither overlap nor touch.
2. Any two image distribution keepout boxes shouldn’t touch nor overlap. Leave a gap so as to be able to make a connecting pattern slightly overlapping with two images. Use 500nm overlap.
3. Place the center of image distributions keepout box at coordinates of integer multiples of 8 um in the die image. (Note: If an image goes to multiple positions, the coordinates should be multiples of 8 to use the same flux trap pattern, e.g. capacitors at multiple locations.
4. (optional if #3 is enforced) Each image has its own flux trap. For this, the center of the Image distribution keepout box should be used to calculate how much flux trap should be offset.

Making flux trap:
1. Before creating flux trap, create backup (klayout could crash).

Layer info
It is very important to understand first what each layer is for, and to use the right layer for whatever you draw in Klayout.

Convention
A layer is specified by N/M, where N=layer number, M = datatype number.

In 0/x layer, anything that doesn’t appear on the mask, e.g. OUTLINES
In 1/x layer, anything that appears on the mask, e.g. flux trap.
Data type defines what kind of stuff goes on an each layer.

Layer definition

Layer name	Layer/Data type	Description
Patch Bbox / IMAGE DIST BBOX	0/0	Image Distribution Bounding Box that defines area in which an image is distributed in the base pattern of a die. Also, it’s used when creating flux traps. Patch bounding box is depreciated. IMAGE DIST BBOX is depreciated because an image distribution bounding box can be replaced by just a box in KEEPOUT layer. Use KEEPOUT.
KEEPOUT	0/1	KEEPOUT contains patterns that keep out FLUX TRAP. In general, all cells such as CPWs and qubit pockets should have KEEPOUT.
CPW path / OUTLINE	0/2	OUTLINE contains any pattern which can be used to create actual images, but do not appear in the IMAGE layer. For example, a guiding path to make a Pcell, guiding shapes, any outlines that is helpful to draw a certain image. Can be a garbage-collecting layer.
IMAGE BBOX	0/3	IMAGE BBOX contains image bounding boxes. Flux traps are created only inside image bounding boxes. The size of the image bounding box should be the same as that of the KEEPOUT box, which should be used as a placeholder for image distribution.
Die BBox	0/4	Die bounding box. This may set the size of actual die, e.g. 6.25x6.25 or 8x8 mm chip / Depreciated. Use IMAGE BBOX.
IMAGE	1/0	Any pattern other than flux trap to be written on the mask
FLUX TRAP	1/1	Flux trap holes (hole size = 4x4 um^2, center-to-center = 8 um)

Do initial setting in Klayout
1. File menu → Setup
a. Default Grids : 1, 0.1, 0.01, 0.001
b. Snapping : Choose both “Snap to grid” and “Snap to edge/vertex”.
2. View menu → Select Top Level Objects
3. File menu → Load Layer Properties → “LayerPropertyFilev2”

Tentative procedure for designing a mask
1. Outline a circuit. Determine a Die Image for base layout. Make it a cell.
2. Make images other than Die Images, and make them all cells.
IMPORTANT:
a. Each cell should have the origin in the center of the image bounding box.
b. Each image shouldn’t have child cell (flatten cell and remake cell if	necessary).
3. Create flux trap for all images.
4. Lay out images for a full mask pattern to make a new cell (call it “mask cell”). Make sure there is at least 750um spacing between images.
5. Record x and y coordinates of the center of image bounding boxes, and the size of them in the mask coordinate.
6. Record x and y coordinates of the Image distribution keepout boxes in the Die Image coordinate.
7. Try simulating one test die by placing images in a Die Image using only recorded coordinates.
8. Flatten the mask cell and save it as a GDS2 file. You’re all set!

Note on Flux trap creation
1. For GND flux trap on a die
Create an instance of fluxTrap_8x8mm and then fluxTrap array. Flatten it and center it. Do boolean operation in layer menu. CHOOSE “no undo buffering”. Otherwise, the GDS file could be corrupted to 0 byte.
2. For flux trap in the images
Each image must be a cell. Even a cell with a sub-PCell is ok. Found that the resulting cell has flattened structure. No need to flatten subcells before creating flux traps.
(Perhaps, no need to distinguish die and image….)

Design Rule Check (DRC)
TO-DO: set up DRC. May need a script.
1. For each cell, check if origin is in the center of bounding box.
2. a No overlap between objects on the same layer, but they can touch.
    b. No overlap between objects in “IMAGE” layer and flux traps in FLUX TRAP	layer.
3. Image distribution keepout boxes should NOT touch. We need about 500nm of image extension into the Image distribution keepout box to avoid unwanted break that could happen during mask production, especially, Cr etching.
4. The center of image bounding box is multiple of 8.